## Slide 1: Notes: Optimizing Network Provisioning through Cooperation [1]
II. Challenges
I. Applications
Provision Wide-Area Network (WAN) bandwidth capacity in inter-data center (DC) for first-party applications in cloud-scale services.
Provide PERFECT amount of bandwidth for immediate and deferrable applications within desired applications’ deadlines.
[1] https://www.usenix.org/conference/nsdi22/presentation/sharma
Figure source: Figure 2 in [1].
The headroom and the valleys represent capacity that could be used to accommodate background demand and reduce total provisioned capacity.
Provisioned capacity.
Larger capacity, higher costs.

## Slide 2: Notes: Optimizing Network Provisioning through Cooperation [1]
III. Methods
Based on knowledge of the application’s deadline coupled with network link failure statistics, the methods optimize network provision by ensuring that application demands are accommodated with the desired satisfaction probability.
[1] https://www.usenix.org/conference/nsdi22/presentation/sharma
D: demand or request, each has a demand satisfaction probability p, and ordered by the value of p:
If cutoff probability is p2, all the corresponding demands up to p2 will be provisioned.
Sort to increasing order
A, B, and C are nodes representing data centers.
L1-L4 are links with provisioned capacities between centers.
Example:
Definitions:
Link L1 fails on day 15th and comes back on day 17th.
Summary:
Each p associates with a set of failure scenarios

## Slide 3: Notes: Optimizing Network Provisioning through Cooperation [1]
III. Methods
Based on knowledge of the application’s deadline coupled with network link failure statistics, the methods optimize network provision by cooperating between application and network, and by ensuring that application demands are accommodated with the desired satisfaction probability.
[1] https://www.usenix.org/conference/nsdi22/presentation/sharma
D: demand or request, each has a demand satisfaction probability p, and ordered by the value of p:
If cutoff probability is p2, all the corresponding demands up to p2 will be provisioned.
Sort to increasing order
A, B, and C are nodes representing data centers.
L1-L4 are links with provisioned capacities between centers.
Example:
Definitions:
Link L1 fails on day 15th and comes back on day 17th.
Summary:
Each p associates with a set of failure scenarios
c
c

## Slide 4
III. Methods
Notes: Optimizing Network Provisioning through Cooperation [1]
[1] https://www.usenix.org/conference/nsdi22/presentation/sharma
A, B, and C are nodes representing data centers.
L1-L4 are data links between centers.
Example: Accommodating capacity for immediate demand with failure scenarios
L1 | L2 | L3 | L4
6 | 6 | 3 | 3
Capacity for Immediate demand
L1 | L2 | L3 | L4
6 | 6 | 3 | 3
Baseline method:
Proposed method:

## Slide 5
Notes: Optimizing Network Provisioning through Cooperation [1]
[1] https://www.usenix.org/conference/nsdi22/presentation/sharma
Baseline method:
L1 | L2 | L3 | L4
6 | 6 | 3 | 3
Capacity for Immediate demands
L1 | L2 | L3 | L4
6 | 6 | 3 | 3
III. Methods
Failure Scenario L1:[15, 17] means: link L1 fails on day 15th and comes back on day 17th.
Augmented capacity for deferrable demands, given the failure scenarios of links.
Proposed method:

## Slide 6
Notes: Optimizing Network Provisioning through Cooperation [1]
[1] https://www.usenix.org/conference/nsdi22/presentation/sharma
Baseline method:
L1 | L2 | L3 | L4
6 | 6 | 3 | 3
Capacity for Immediate demands
L1 | L2 | L3 | L4
6 | 6 | 3 | 3
III. Methods
Failure Scenario L1:[15, 17] means: link L1 fails on day 15th and comes back on day 17th.
Augmented capacity for deferrable demands, given the failure scenarios of links.
Proposed method:
Summary：
Satisfy the cost function (1) with constraints A, B and C, equations (2) –(5).

## Slide 7
III. Methods
Notes: Optimizing Network Provisioning through Cooperation [1]
[1] https://www.usenix.org/conference/nsdi22/presentation/sharma

## Slide 8
III. Methods
Notes: Optimizing Network Provisioning through Cooperation [1]
[1] https://www.usenix.org/conference/nsdi22/presentation/sharma

## Slide 9
III. Methods
Notes: Optimizing Network Provisioning through Cooperation [1]
[1] https://www.usenix.org/conference/nsdi22/presentation/sharma

## Slide 10: Notes: Optimizing Network Provisioning through Cooperation [1]
[1] https://www.usenix.org/conference/nsdi22/presentation/sharma
IV. Conclusions
Reduce provisioned network capacity signiﬁcantly, with savings ranging from 30% to 45%, while supporting specific demands, and improving link utilization compared to the baseline.
Remain effective even when used with demand forecasts.
In an example, Baseline provisioning requires 30 GB/day total capacity augments whereas the proposed method Application-informed Provisioning (Approv) requires only 6.67 GB/day total capacity augments.
Baseline method:
L1 | L2 | L3 | L4
6 | 6 | 3 | 3
Capacity for Immediate demands
L1 | L2 | L3 | L4
6 | 6 | 3 | 3
Proposed method:
Total augmented capacity: 30 6.67
Augmented capacity for deferrable demands, given the failure scenarios of links.
Limitations: