## Slide 1: Title: Running ML in Small Wireless and/or Batteryless IoT Devices[1]
Problems
Solutions
Results
Contactless Seismocardiography via Deep Learning Radars [2]
WiStress: Contactless Stress Monitoring using Wireless Signals [3]
Self-Reconfigurable Micro-Implants for Cross-Tissue Wireless and Batteryless Connectivity [4]
Towards Battery-Free Machine Learning and Inference in Underwater Environments[5]
Hybrid architecture combines signal processing with deep learning, including 3 CNNs in different steps:
1.1 Use 1D CNN to detect the template of heart rate histogram.
1.2 Combine with 1.1 to do beamforming (controls phase and relative amplitude of signal at each transmitter to create a pattern of constructive and destructive interference in the wavefront[7]) and locate human heart and SNR improvement.
2. Use 2nd CNN to get RF-to-SCG signal translator
3. Use 3rd CNN to label key cardiovascular events , pass work [6]
Stress monitoring by heartbeat intervals. Challenges: user’s body movements.
Based on [2], adding self-similarity matrix (SSM) can detect and filter user’s body movements. Figure 5 in [3] 2D shows SSM of a 1D signal array. In this array, when the more 2 signals are alike, the higher the similarity.
high accuracy (84%-95%)
RF signals amplitude decays linearly with distance in air, but exponentially in human tissues; existing designs lack of scalability, are limited to shallow depths.
Two key innovations (Figure 4 and 6 in [4]):
1. A reprogrammable antenna (according to specific frequency band of interest) that can tune its energy harvesting resonance (electrically matching the antenna impedance to the input impedance of the rectifier to boosts harvesting energy efficiency by minimizing losses) to surrounding tissues.
2. A backscatter rate adaptation protocol.
Tune energy harvesting resonance by more than 200 MHz, scale bitrate by an order of magnitude up to 6Mbps to support higher data rate applications (such as streaming low-res images)
Major Steps:
1. Employ piezoelectric materials, which convert mechanical energy (i.e. sound) to electrical energy, and use multi-stage rectifier to rectify AC to a DC voltage.
2. Lightweight DNN model that can recognize marine mammals from their sounds.
3. Send the result via backscatter to a remote receiver.
Design and build battery-free devices capable of machine learning and inference in underwater environments.
Feasibility of performing sensing and inference.
Record seismocardiogram (SCG, including 5 key cardiovascular events) by wireless reflection via radiofrequency (RF). Challenge: identify human (and heart rate) among other objects in a space.
Detect five key cardiovascular events with a median error between 0.26%-1.29%.
Opportunities:
1. Battery-free on-device personalization for different testing data from IoT network.
2. Considering the diversity of IoT devices, task-specific hardware components for DNN models in ultra-low power MCUs (microcontroller units).
3. Battery-free distributed ML training for life-long ML with up-to-date data.
[1] http://www.mit.edu/~fadel/publications.html
[2] https://dl.acm.org/doi/10.1145/3372224.3419982
[3] https://dl.acm.org/doi/10.1145/3478121
[4] https://dl.acm.org/doi/10.1145/3372224.3419216
[5] https://arxiv.org/abs/2202.08174
[6] https://arxiv.org/abs/1505.04597
[7] https://en.wikipedia.org/wiki/Beamforming

## Slide 2: 标题：可运行ML的小型无线和/或无电池IoT设备[1]
问题
方法
结果
Contactless Seismocardiography via Deep Learning Radars [2]
WiStress: Contactless Stress Monitoring using Wireless Signals [3]
Self-Reconfigurable Micro-Implants for Cross-Tissue Wireless and Batteryless Connectivity [4]
Towards Battery-Free Machine Learning and Inference in Underwater Environments[5]
信号处理和深度学习结合的混合结构, 包括3个不同作用的CNN：
1.1 使用1维CNN去找心跳直方图的模板
1.2 结合1.1的结果做波束成型(beamforming, 通过控制信号的相位和幅度去产生相消和相长的干涉模式，以达到最佳传输效果[7])以检测心脏位置和心跳，并进行信噪比改善。
2. 使用第二个CNN进行从RF信号到SCG信号的转换。
3. 使用第三个CNN标注SCG中5种心血管活动(这里采用了[6]的方法)。
通过心跳间隔(heartbeat intervals or IBIs)测量精神压力状态。难点：分辨和去除用户身体移动引起的信号干涉。
在[2]的基础上加入了自相关矩阵(self-similarity matrix, SSM) 从而区别心跳活动信号和身体移动引起的干涉信号。如[3]中图5显示，由1维信号组成的2维SSM。 同组两点信号越相似，值在SSM中越大。
84%-95%的高准确率。
RF信号的振幅在空气中是直线衰退，到了人体组织是指数消减; 现有的设计缺乏可扩展性，信号只能到达表皮。
文章作者有两个主要的发明 ([4]中图4和图6)：
1. 设计可根据感兴趣的特定频段进行编程的天线，用以调整其为收集能量而在周围组织产生的共振 (resonance, 匹配天线阻抗与整流器的输入阻抗以达到最小化损耗来提高能量收集效率)。
2. 反向散射率自适应协议。
能量收集共振调谐超过 200 MHz（适应不同的组织），比特率增加最高可达 6Mbps，使其能够支持更高数据速率的应用（例如低分辨率图像视频）。
设计总结：
1. 采用压电材料，将声音机械能转换为电能, 并使用多级整流器将交流电整流为直流电压。
2. 可以从声音中识别海洋哺乳动物的轻量级 DNN 模型。
3. 通过反向散射将结果发送到远程接收器。
设计和制造能够在水下环境中进行机器学习和推理的无电池设备。
可执行水下感应和推理操作。
基于无线电频率(radiofrequency, RF), 通过wireless reflection产生心震图(seismocardiogram, SCG, 其包括5种主要的心血管活动). 难点: 在一个有多种物件的环境里确定接收目标(人)并记录心跳。
成功检测5种重要心血管活动，错误中值为0.26%-1.29%。
未来研究机会:
1. 根据分布式网络中各点数据差异，进行无电池设备个性化。
2. 考虑到IoT设备的多样性，设计处理特定任务的硬件组件，使DNN 模型可在超低功耗的 MCU（微控制器单元）上运行。
3. 使用无电池的端侧设备进行分布式ML 训练可促进端侧的终身学习使用最新采集到的数据。
[1] http://www.mit.edu/~fadel/publications.html
[2] https://dl.acm.org/doi/10.1145/3372224.3419982
[3] https://dl.acm.org/doi/10.1145/3478121
[4] https://dl.acm.org/doi/10.1145/3372224.3419216
[5] https://arxiv.org/abs/2202.08174
[6] https://arxiv.org/abs/1505.04597
[7] https://en.wikipedia.org/wiki/Beamforming